## Slide 1: Computer Networks Router Architecture and Scheduling
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Router Architecture

## Slide 3: Router architecture overview
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame

## Slide 4: Input port functions
switch
fabric
line
termination
Physical layer:
Bit-level reception
link
layer
protocol
(receive)
Link layer:
e.g., Ethernet
lookup,
forwarding
queueing
Decentralized switching:
Using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
Goal: complete input port processing at ‘line speed’
Input port queuing: if datagrams arrive faster than forwarding rate into switch fabric
high-speed
switching
fabric
routing
processor
router input ports
router output ports

## Slide 5: Switching fabrics
Transfer packet from input link to appropriate output link
high-speed
switching
fabric
N input ports
N output ports
. . .
. . .
Switching rate: rate at which packets can be transfer from inputs to outputs
  Often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
R
R
R
R
(rate: NR, ideally)

## Slide 6: Switching fabrics
Transfer packet from input link to appropriate output link
Bus
Memory
memory
Interconnection
network
Three major types of switching fabrics:
Switching rate: rate at which packets can be transfer from inputs to outputs
  Often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable

## Slide 7: Switching via memory
First generation routers:
Traditional computers with switching under direct control of CPU
Packet copied to system’s memory
Speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 8: Switching via a bus
Datagram from input port memory to output port memory via a shared bus
Bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access routers

## Slide 9: Switching via interconnection network
Crossbar, Clos networks, other interconnection nets initially developed to connect processors in multiprocessor computer architecture
8x8 multistage switch
built from smaller-sized switches
3x3 crossbar
Multistage switch: nxn switch from multiple stages of smaller switches
Exploiting parallelism:
  Fragment datagram into fixed length cells on entry
  Switch cells through the fabric, reassemble datagram at exit
3x3 crossbar

## Slide 10: Switching via interconnection network
Scaling, using multiple switching “planes” in parallel:
  Speedup, scaleup via parallelism
fabric plane 0
. . .
. . .
fabric plane 1
. . .
. . .
fabric plane 2
. . .
. . .
fabric plane 3
. . .
. . .
fabric plane 4
. . .
. . .
fabric plane 5
. . .
. . .
fabric plane 6
. . .
. . .
fabric plane 7
. . .
. . .
Cisco CRS router:
  Basic unit: 8 switching planes
  Each plane: 3-stage interconnection network
  up to 100’s Tbps switching capacity
Cisco CRS router: https://nexstor.com/wp-content/uploads/2018/05/cisco-crs-1-multishelf-system-datasheet.pdf

## Slide 11: Output port functions
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R
high-speed
switching
fabric
routing
processor
router input ports
router output ports

## Slide 12: Queuing, Buffer management and Scheduling

## Slide 13: Input port queuing
If switch fabric slower than input ports combined  queueing may occur at input queues
  Queueing delay and loss due to input buffer overflow!
Output port contention: only one red datagram can be transferred. lower red packet is blocked
switch
fabric
One packet time later: green packet experiences HOL blocking
switch
fabric
Head-of-the-Line (HOL) blocking: Queued datagram at front of queue prevents others in queue from moving forward

## Slide 14: Output port queuing
Buffering required when datagrams arrive from fabric faster than link transmission rate
Drop policy: which datagrams to drop if no free buffers?
Scheduling discipline chooses among queued datagrams for transmission
Datagrams can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R

## Slide 15: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT times link capacity C
  e.g., RTT = 250 msec, C = 10 Gbps link  2.5 Gbit buffer
  Delay-bandwidth product
Too much buffering will reduce packet loss, but can increase delays
  Long RTTs: poor performance for real-time apps, sluggish TCP response
More recent recommendation: with N flows, buffering equal to
Notes: You might think that more buffering is a good thing. Buffering is a bit like salt—just the right amount of salt makes food better, but too much makes it inedible!

## Slide 16: Buffer Management
Buffer management:
Drop: which packet to add, drop when buffers are full
  Tail drop: drop arriving packet
  Priority: drop/remove on priority basis
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
scheduling
Marking: which packets to mark to signal congestion (i.e. ECN)
R
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R

## Slide 17: Packet Scheduling: FCFS
Packet scheduling: deciding which packet to send next on link
  First come, first served
  Priority based
  Round robin
  Weighted fair queueing
FCFS: packets transmitted in order of arrival to output port
also known as: First-in-first-out (FIFO)
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R

## Slide 18: Scheduling policies: Priority Based
Priority based scheduling:
Arriving traffic classified, queued by class
  Any header fields can be used for classification
high priority queue
low priority queue
arrivals
classify
departures
link
1
3
2
4
5
arrivals
departures
packet in service
Send packet from highest priority queue that has buffered packets
  FCFS within priority class
1
3
4
2
5
1
3
2
4
5

## Slide 19: Scheduling policies: round robin
Round Robin (RR) scheduling:
Arriving traffic classified, queued by class
  Any header fields can be used for classification
classify
arrivals
departures
link
R
Server cyclically, repeatedly scans class queues, sending one complete packet from each class (if available) in turn

## Slide 20: Scheduling policies: Weighted Fair Queueing
Weighted Fair Queuing (WFQ):
Generalized Round Robin
classify
arrivals
departures
link
R
w1
w2
w3
Minimum bandwidth guarantee (per-traffic-class)
Each class , has weight, and gets weighted amount of service in each cycle:

## Slide 21: Summary
Router architecture, queuing and packet scheduling:
  Router architecture
    Input ports
    High speed fabric
    Out ports
  Packet scheduling
    FCFS
    Priority based
    Round robin
    Weighted fair queuing