## Slide 1: Computer Networks I Data Link Control Protocols (Flow Control)
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Data Link Layer
Data link layer has responsibility of transferring datagram from one node to physically adjacent node over a link
  Framing
    Encapsulate datagram into frame, adding header, trailer
  Reliable delivery between adjacent nodes
    Flow control and error control
  Channel access if shared medium

## Slide 3: Data Link Layer
Application
Network
Link
Transport
Physical
Sending side:
Encapsulates datagram in frame
Adds error checking bits, reliable data transfer, flow control, etc.
Receiving side:
Looks for errors, reliable data transfer, flow control, etc.
Extracts datagram, passes to upper layer at receiving side
linkh
datagram
datagram
Application
Network
Transport
Link
Physical
datagram

## Slide 4
Data Link Layer
Controller
Physical
CPU
Memory
host bus
(e.g., PCI)
Network interface
Application
Transport
Network
Link
Link
Physical
Link layer implemented on-chip or in network interface card (NIC)
  Implements link, physical layer
  Attaches into host’s system buses
Combination of hardware, software, firmware

## Slide 5: Flow Control

## Slide 6: Flow Control
Flow control assures that a transmitting entity does not overwhelm a receiving entity with data
  If the transmitter transmits too fast, then the receiver buffer may overflow
    This may lead to data loss, retransmission, and performance reduction
Application
Network
Transport
Link
Physical
Application
Network
Transport
Link
Physical

## Slide 7: Flow Control
Flow control assures that a transmitting entity does not overwhelm a receiving entity with data
  Assumptions:
    No frames loss or error, all transmitted frames are successfully received
    Transmitted frames suffers from an arbitrary and variable amount of delay
Application
Network
Transport
Link
Physical
Application
Network
Transport
Link
Physical

## Slide 8: Flow Control
Flow control:
  Stop and Wait Flow Control
  Sliding Window Flow Control
Application
Network
Transport
Link
Physical
Application
Network
Transport
Link
Physical

## Slide 9: Stop-and-Wait Flow Control

## Slide 10: Stop and Wait Flow Control
Source:
  Source transmits a DATA frame
  Source waits for ACK frame before sending next DATA frame
Destination:
  Destination receives DATA frame  replies back with an ACK if ready to accept more data
  Destination can stop flow of data by withholding ACK

## Slide 11: Efficiency Calculation

## Slide 12: Efficiency Calculation
Stop-and-wait allows only 1 frame to be in transit at a time
  Leads to serious inefficiencies especially when the frame size is small
  Efficiency can be greatly improved by allowing multiple frames to be in transit at a time  which is the idea of Sliding-window flow control

## Slide 13: Sliding Window Flow Control

## Slide 14: Sliding Window Flow Control
Receiver allocates a buffer space of W frames
Sender can send up to W frames without waiting for an ACK
Each frame is labeled with a k-bit sequence number
  Frames are numbered modulo 2k
  Giving max window size of up to 2k – 1 (will learn during error control)
Receiver acknowledges a frame by sending an ACK (or Receiver Ready, RR)
ACK includes the sequence number of the next frame expected
  ACK also implicitly says that the receiver can receive the next W frames

## Slide 15: Sliding Window Flow Control

## Slide 16: Sliding Window Flow Control
  Sender and Receiver record:
    Last frame acknowledged
    Last frame transmitted (in case of sender) or received (in case of receiver)
    Window of frames that may be transmitted (in case of sender) or received (in case of receiver)

## Slide 17: Sliding Window Flow Control: Example

## Slide 18: Sliding Window Flow Control
Additional features:
  Receive Not Ready (RNR): Receiver can ACK frames without permitting further transmission
  RNR 5: received frames up to 4, but unable to accept any more
  Must send a normal acknowledge to resume
  Piggybacking: If a station has a DATA and ACK to send, it sends both together  saves communication capacity
  DATA frame includes sequence number of the frame and sequence number used for ACK (i.e. next expected frame number)
  If the station has an ACK but no DATA to send, it sends normal ACK (RR or RNR)
  If the station has DATA to send but no new ACK  repeats the last ACK seq. no.

## Slide 19: Sliding Window Flow Control

## Slide 20: Summary
Link layer services
Flow control in Link Layer:
  Stop and wait
  Sliding window