## Slide 1: Computer Networks I Data Link Control Protocols (Error Control)
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Error Control
Two types of error
  Lost frame: A frame fails to arrive at the other end
  Damaged frame: A frame arrives at the destination, but few bits are damaged
Automatic Repeat Request (ARQ):
  Stop-and-wait ARQ
  Go-back-N ARQ
  Selective-reject ARQ

## Slide 3: Stop-and-Wait ARQ

## Slide 4: Stop-and-Wait ARQ
Based on Stop-and-Wait flow control
Source:
  Source transmits single frame, waits for an ACK
  It also starts a timer and maintains the copy
  If ACK received, stop timer and transmit next frame
  Sender has timeout  if no ACK within timeout, retransmit
Destination:
  Destination sends ACK if frame received correctly (with no errors)
  If frame received is damaged, discard it

## Slide 5: Stop-and-Wait ARQ
If ACK is damaged, transmitter will not recognize
  Transmitter will retransmit after the timeout
  Receiver gets two copies of frame
  Solution: use 1-bit frame SEQ number and ACK0 / ACK1
Stop-and-Wait ARQ is simple, but inefficient

## Slide 6: Stop-and-Wait ARQ

## Slide 7: Go-Back-N ARQ

## Slide 8: Sliding Window Flow Control: Example

## Slide 9: Go-Back-N ARQ
Based on Sliding Window flow control  Most commonly used error control
Source:
  Sender must go back and retransmit that frame and all subsequent frames
  If no ACK received from Destination after timeout, the Source can retransmit the previous frame asked by the receiver
Destination:
  If no error, the destination will ACK incoming frames as in sliding window
    RR=receive ready, or piggybacked acknowledgment with sequence number of next expected frame
  If the destination station detects an error in a frame, it may send a negative acknowledgment
    REJ=reject with sequence number of next expected frame
  Destination will discard that frame and all future frames until the frame in error is received correctly

## Slide 10: Go-Back-N ARQ
Frame 5

## Slide 11: Go-Back-N ARQ
A k-bit sequence number provides a sequence number range of 2k
  However the maximum window size is limited to 2k - 1
As a case of 3-bit sequence number (i.e. sequence number space is 8)
Suppose sender sends frame 0 and gets back an RR 1
Then sends frames 1, 2, 3, 4, 5, 6, 7, 0 and gets another RR 1
This could mean that all eight frames were received correctly and the RR 1 is a cumulative acknowledgment
It could also mean that all eight frames were damaged or lost in transit, and the receiving station is repeating its previous RR 1
The problem is avoided if the maximum window size is limited to 7, i.e. 23 - 1
Max window size = 2k – 1 (for a k-bit sequence number)

## Slide 12: Selective Reject ARQ

## Slide 13: Selective Reject ARQ
Also called selective retransmission
Only rejected or timeout frames are retransmitted
Subsequent frames are accepted by the receiver and buffered
Pros:
  Minimizes retransmission
Cons:
  Receiver must maintain large enough buffer to store out-of-order frames
  More complex logic in transmitter
Less widely used
Useful for satellite links with long propagation delays

## Slide 14: Selective Reject ARQ
Frame 7

## Slide 15: Selective Reject ARQ
Window size is more restrictive for selective-reject than for go-back-N
Consider the case of a 3-bit sequence number size for selective-reject
  Sender sends frames 0 through 6
  Receiver receives all seven frames and cumulatively acknowledges with RR 7
  Because of a noise burst, the RR 7 is lost
  Sender times out and retransmits frame 0
  Receiver has already advanced its receive window to accept frames 7, 0, 1, 2, 3, 4, and 5
  It assumes that frame 7 has been lost and that this is a new frame 0, which it accepts
The problem is that there is an overlap in between the sending and receiving window
  To overcome the problem, the maximum window size should be no more than half the range of sequence numbers
Max window size = 2k-1 (for a k-bit sequence number)

## Slide 16: Comparison
Stop and Wait
Sliding Window
Go-back N
Selective Reject
Stop and Wait
Flow control
Error control

## Slide 17: Comparison

## Slide 18: Summary
Error control in Link Layer:
  Stop and wait
  Selective reject
  Go-back N