## Slide 1: Computer Networks I IPv4 Datagram Format and Addressing
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: IPv4 Datagram Format

## Slide 3: IPv4 Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 4: IP Fragmentation/Reassembly
Network links have MTU (max. transfer size) - largest possible link-level frame
  Different link types, different MTUs
  Ethernet 1.5 KB, WiFi 2.3 KB
Large IP datagram divided (“fragmented”) within net
  One datagram becomes several datagrams
  Reassembled only at destination
  IP header bits used to identify, order related fragments
Fragmentation:
In: one large datagram
Out: 3 smaller datagrams
reassembly
…
…

## Slide 5: IP Fragmentation/Reassembly
ID
=x
offset
=0
MF
=0
length
=4000
ID
=x
offset
=0
MF
=1
length
=1500
ID
=x
offset
=185
MF
=1
length
=1500
ID
=x
offset
=370
MF
=0
length
=1040
one large datagram becomes
several smaller datagrams
Example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 6: IP Fragmentation/Reassembly
However fragmentation is undesirable
More overhead for the routers
Solution: discover the MTU that will fit for all the links
  Implemented using ICMP  DF bit is set to 1

## Slide 7: IP Addressing

## Slide 8: IP addressing: introduction
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
IP address: 32-bit identifier associated with each host or router interface
Interface: connection between host/router and physical link
  Router’s typically have multiple interfaces
  Host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
Dotted-decimal IP address notation:

## Slide 9: Subnets
IP addresses have structure:
  Network part: devices in same network have common high order bits
  Host part: remaining low order bits

## Slide 10: IP addressing: Classful Addressing
Classful Addressing: Fixed number of bits for network and host address
  Used in old days

## Slide 11: IP addressing: Classful Addressing
Classful Addressing: Fixed number of bits for network and host address
  Used in old days
Network address: All 0’s in the host address part
  Class-A: 01111111.00000000.00000000.00000000 or 127.0.0.0
  Class-B: 10101000.10101100.00000000.00000000 or 168.172.0.0
  Class-C: 11011000.01111011.10010001.00000000 or 216.123.145.0
Broadcast address: All 1’s in the host address part
  Class-A: 01111111.11111111.11111111.11111111 or 127.255.255.255
  Class-B: 10101000.10101100.11111111.11111111 or 168.172.255.255
  Class-C: 11011000.01111011.10010001.11111111 or 216.123.145.255

## Slide 12: IP addressing: Classful Addressing
How many hosts can a Class A, Class B and Class C address accommodate?
  Class-A:
  Class-B:
  Class-C:

## Slide 13: Limitation of Classful Addressing
Suppose you have 300 hosts. Which IP address you will go for?
  Class-C: Less addresses
  Class-B: Huge wastage of IP addresses

## Slide 14: IP addressing: CIDR
CIDR: Classless InterDomain Routing (pronounced “cider”)
  Network or subnet portion of address of arbitrary length
  Address format: a.b.c.d/x, where x is # bits in network or subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23
Src: https://commons.wikimedia.org/wiki/File:Subnetting_operation.svg

## Slide 15: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
What’s a subnet ?
  Device interfaces that can physically reach each other without passing through an intervening router
Network consisting of 3 subnets

## Slide 16: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Recipe for defining subnets:
Detach each interface from its host or router, creating “islands” of isolated networks
Each isolated network is called a subnet
subnet mask: /24
(high-order 24 bits: subnet part of IP address)
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24

## Slide 17: Subnets
Where are the subnets?
What are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.8/24

## Slide 18: Subnets
CS: 550
EE: 550
Art: 400
CS
EE
Art
128.208.0.0/16
Useful Link: https://www.cisco.com/c/en/us/support/docs/ip/dynamic-address-allocation-resolution/13711-40.html

## Slide 19: Subnets: Fixed Length Subnetting
CS: 60
EE: 10
Art: 10
Art
CS
EE
206.12.10.0/24

## Slide 20: Subnets: Variable Length Subnetting
CS: 60
EE: 10
Art: 10
CS
EE
Art
206.12.10.0/24

## Slide 21: Aggregation of IP Prefixes
University | First address | Last address | How many | Prefix
Cambridge | 194.24.0.0 | 194.24.7.255 | 2048 | 194.24.0.0/21
Edinburgh | 194.24.8.0 | 194.24.11.255 | 1024 | 194.24.8.0/22
(Available) | 194.24.12.0 | 194.24.15.255 | 1024 | 194.24.12.0/22
Oxford | 194.24.16.0 | 194.24.31.255 | 4096 | 194.24.16.0/20

## Slide 22: Summary
Internet Protocols:
  IPv4 datagram format
  Fragmentation and Reassembly
  IP addressing
    Classful addressing
    Classless InterDomain Routing