## Slide 1: Computer Networks II Application Layer Web and Electronic Mail
Amitangshu Pal
Computer Science and Engineering
IIT Kanpur

## Slide 2: Web and HTTP

## Slide 3: Web and HTTP
Web page consists of objects
Object can be HTML file, JPEG image, Java applet, audio file,…
Web page consists of base HTML-file which includes several referenced objects
Each object is addressable by a URL, e.g.,
http://en.Wikipedia.org/somePage/pic.gif
Server
Page on server
Protocol

## Slide 4: HTTP Overview
HTTP: Hypertext transfer protocol
Web’s application layer protocol
Client/server model
  Client: Browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  Server: Web server sends (using HTTP protocol) objects in response to requests
PC running
Firefox browser
Server
running
Apache Web
server
iPhone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 5: HTTP Overview
Uses TCP:
Client resolves server to IP address (DNS)
Client initiates TCP connection (creates socket) to server, port 80
Server accepts TCP connection from client
HTTP messages (application-layer protocol messages) exchanged between browser (HTTP client) and Web server (HTTP server)
TCP connection closed
HTTP is “stateless”
Server maintains no information about past client requests

## Slide 6: HTTP Request Message
Two types of HTTP messages: request, response
Header lines
GET /index.html HTTP/1.1\r\n
Host: www-net.cs.umass.edu\r\n
User-Agent: Mozilla/5.0 (Macintosh; Intel Mac OS X 10.15; rv:80.0) Gecko/20100101 Firefox/80.0 \r\n
Accept: text/html,application/xhtml+xml\r\n
Accept-Language: en-us,en;q=0.5\r\n
Accept-Encoding: gzip,deflate\r\n
Connection: keep-alive\r\n
\r\n
carriage return character
line-feed character
Request line (GET, POST,
HEAD commands)
Carriage return, line feed at start of line indicates end of header lines

## Slide 7: HTTP Response Message
Status line (protocol
status code status phrase)
Header lines
Data, e.g., requested
HTML file
HTTP/1.1 200 OK
Date: Tue, 08 Sep 2020 00:53:20 GMT
Server: Apache/2.4.6 (CentOS) OpenSSL/1.0.2k-fips PHP/7.4.9 mod_perl/2.0.11 Perl/v5.16.3
Last-Modified: Tue, 01 Mar 2016 18:57:50 GMT
ETag: "a5b-52d015789ee9e"
Accept-Ranges: bytes
Content-Length: 2651
Content-Type: text/html; charset=UTF-8
\r\n
data data data data data ...

## Slide 8: HTTP Response Status Codes
200 OK
  Request succeeded, requested object later in this message
301 Moved Permanently
  Requested object moved, new location specified later in this message (in Location: field)
400 Bad Request
  Request msg not understood by server
404 Not Found
  Requested document not found on this server
505 HTTP Version Not Supported
Status code appears in 1st line in server-to-client response message
Some sample codes:

## Slide 9: Non-persistent HTTP (HTTP 1.0)
Non-persistent HTTP
At most one object sent over TCP connection
  Connection then closed
Downloading multiple objects required multiple connections

## Slide 10: Non-persistent HTTP (HTTP 1.0): Response Time
HTTP response time:
One RTT to initiate TCP connection
One RTT for HTTP request and first few bytes of HTTP response to return
File transmission time
Non-persistent HTTP response time =
  2RTT+ file transmission time
Time to
transmit
file
Initiate TCP
connection
RTT
Request
file
RTT
File
received
time
time

## Slide 11: Non-persistent HTTP (HTTP 1.0): Response Time
Non-persistent HTTP issues:
Requires 2 RTTs per object
OS overhead for each TCP connection
Browsers often open parallel TCP connections to fetch referenced objects
Time to
transmit
file
Initiate TCP
connection
RTT
Request
file
RTT
File
received
time
time

## Slide 12: Non-persistent HTTP (HTTP 1.0): Response Time
We are downloading a webpage having a base HTML file with 5 embedded objects:
All objects are from the same server
The transmission time is negligible
Objects are requested sequentially
Object requests are made in parallel
Time to
transmit
file
Initiate TCP
connection
RTT
Request
file
RTT
File
received
time
time

## Slide 13: Persistent HTTP (HTTP 1.1)
Persistent HTTP
Multiple objects can be sent over single TCP connection between client, server
Server leaves connection open after sending response
Subsequent HTTP messages between same client/server sent over open connection

## Slide 14: Persistent HTTP (HTTP 1.1)
Persistent HTTP
Non-pipelined:
  Response time of downloading a HTML file with 5 embedded objects
Pipelined: Multiple requests can be sent together

## Slide 15
Non-persistent HTTP
Persistent HTTP (sequential)
Persistent HTTP (pipelined)

## Slide 16: HTTP 1.1
HTTP1.1: Introduced multiple, pipelined GETs over single TCP connection
Server responds in-order (FCFS: first-come-first-served scheduling) to GET requests
With FCFS, small object may have to wait for transmission (head-of-line (HOL) blocking) behind large object(s)
Notes: t’

## Slide 17: HTTP 1.1 (HOL Blocking)
Client
Server
GET O1
GET O2
GET O3
GET O4
O1
O2
O3
O4
Object data requested
O1
O2
O3
O4
Objects delivered in order requested: O2, O3, O4 wait behind O1
HTTP 1.1: client requests 1 large object (e.g., video file) and 3 smaller objects
Notes: t’

## Slide 18: HTTP/2
HTTP/2: [RFC 7540, 2015] Increased flexibility at server in sending objects to client:
Methods, status codes, most header fields unchanged from HTTP 1.1
Transmission order of requested objects based on client-specified object priority (not necessarily FCFS)
Push unrequested objects to client
Divide objects into frames, schedule frames to mitigate HOL blocking
Key goal: Decreased delay in multi-object HTTP requests
Notes: t’

## Slide 19: HTTP/2: Mitigating HOL Blocking
Client
Server
GET O1
GET O2
GET O3
GET O4
O2
O4
Object data requested
O1
O2
O3
O4
O2, O3, O4 delivered quickly, O1 slightly delayed
O3
O1
HTTP/2: objects divided into frames, frame transmission interleaved
Notes: shortest job first: decreased average delay!

## Slide 20: Cookies
client
server
usual http response msg
usual http response msg
cookie file
one week later:
usual http request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
usual http request msg
Amazon server
creates ID
1678 for user
create
entry
usual http response
set-cookie: 1678
ebay 8734
amazon 1678
usual http request msg
cookie: 1678
cookie-
specific
action
access
ebay 8734
amazon 1678
backend
database

## Slide 21: User-server State: Cookies
Many Web sites use cookies
Four components:
  1) Cookie header line of HTTP response message
  2) Cookie file kept on user’s host, managed by user’s browser
  3) Cookie header line in next HTTP request message
  4) Back-end database at Web site
Example:
An user visits specific e-commerce site for first time
When initial HTTP requests arrives at site, site creates:
  Unique ID
  Entry in backend database for ID

## Slide 22: Cookies (continued)
What cookies can be used for:
Authorization
Shopping carts
Recommendations
User session state (Web e-mail)

## Slide 23: Web Caches

## Slide 24: Web caching (Browser cache + Proxy cache)
User often revisit same pages
Goal: Satisfy client request without involving origin server

## Slide 25: Web caching (Browser cache + Proxy cache)
Why Web caching?
Reduce response time for client request
Reduce traffic on an institution’s access link

## Slide 26: How to verify if cached content is up-to-date?
Server tells cache about object’s allowable caching in response header:
Cache-control: max-age = <seconds>
  Max time until the content is considered fresh
Cache-control: public
  Content is cacheable
Cache-control: private
  Content is cacheable at the browser, but not at the proxy cache
Cache-control: no-cache
  Cache but revalidate
Cache-control: no-store
  No caching

## Slide 27: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
Using Last-Modified + Conditional GET
Cache: specify time of cached copy in HTTP request
  If-modified-since: <time>
Server: response contains no object if cached copy is up-to-date:
  HTTP/1.0 304 Not Modified
HTTP request msg
If-modified-since: <time>
HTTP response
HTTP/1.0
304 Not Modified
object
not
modified
before
<date>
HTTP request msg
If-modified-since: <time>
HTTP response
HTTP/1.0 200 OK
<data>
object
modified
after
<date>
client
server

## Slide 28: Conditional GET
Goal: don’t send object if cache has up-to-date cached version
Using ETag + Conditional GET
Cache: specify Etag (hash) of cached copy in HTTP request
  If-Node-Match: <ETag>
Server: response contains no object if cached copy is up-to-date:
  HTTP/1.0 304 Not Modified
Src: https://commons.wikimedia.org/wiki/File:Etag_header_beispiele.png

## Slide 29: Conditional GET
Goal: don’t send object if cache has up-to-date cached version

## Slide 30: Web caching (Web Proxies)
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
Performance:
Access link utilization = .97
LAN utilization: .0015
End-end delay = RTT + access link delay + LAN delay
= 2 sec + minutes + usecs
Scenario:
Access link rate: 1.54 Mbps
RTT from institutional router to server: 2 sec
Web object size: 100K bits
Average request rate from browsers to origin servers: 15/sec
  Avg data rate to browsers: 1.50 Mbps
Notes: explain why minutes (recall earlier delay versus arrival rate curve from Chapter 1)

## Slide 31: Internet Content Popularity
Zipf distribution (linear scale)
Zipf distribution (log-log scale)

## Slide 32: Web caching (Web Proxies)
origin
servers
public
Internet
institutional
network
1 Gbps LAN
1.54 Mbps
access link
local web cache
Suppose cache hit rate is 0.4:
40% requests served by cache, with low (msec) delay
60% requests satisfied at origin
  Rate to browsers over access link
  = 0.6 * 1.50 Mbps = .9 Mbps
  Access link utilization = 0.9/1.54 = .58 means low (msec) queueing delay at access link
Average end-end delay:
  = 0.6 * (delay from origin servers) + 0.4 * (delay when satisfied at cache) = 0.6 (2 secs) + 0.4 (~msecs) = ~ 1.2 secs
Notes: t’

## Slide 33: Content Distribution Networks (CDNs)

## Slide 34: Video Streaming and CDNs
Stream video traffic: major consumer of Internet bandwidth
  Netflix, YouTube, Amazon Prime: 80% of residential ISP traffic (2020)
Challenges:
  Scale - how to reach ~1B users?
  Heterogeneity
    Different users have different capabilities (e.g., wired versus mobile; bandwidth rich versus bandwidth poor)

## Slide 35: Streaming Stored Video
Video server
(stored video)
client
Internet

## Slide 36: Streaming Stored Video
Video
recorded (e.g., 30 frames/sec)
2. Video
sent
Cumulative data
Streaming: at this time, client playing out early part of video, while server still sending later part of video
time
3. Video received, played out at client (30 frames/sec)
Network delay
(fixed in this example)

## Slide 37: Streaming Stored Video: Challenges
Continuous playout constraint: During client video playout, playout timing must match original timing
  But network delays are variable (jitter), so will need client-side buffer to match continuous playout constraint
Other challenges:
  Client interactivity: pause, fast-forward, rewind, jump through video
  Video packets may be lost, retransmitted

## Slide 38: Streaming Stored Video: Playout Buffering
Constant bit
rate video
transmission
Cumulative data
time
Variable
network
delay
Client video
reception
Constant bit
rate video
playout at client
Client playout
delay
Buffered
video
Client-side buffering and playout delay: compensate for network-added delay, delay jitter

## Slide 39: Content Distribution Networks (CDNs)
Challenge: How to stream content (selected from millions of videos) to hundreds of thousands of simultaneous users?
  Push CDN servers deep into many access networks
    Close to users
    Akamai: 240,000 servers deployed in > 120 countries (2015)
Solution: Store/serve multiple copies of videos at multiple geographically distributed sites (CDN)

## Slide 40: Content Distribution Networks (CDNs)

## Slide 41: Content Distribution Networks: DNS Redirection
http://www.Netflix.com/page.html

## Slide 42: Content Distribution Networks (CDNs)
Win-win solution for all parties:
  Reduces server load  Content providers are 🙂
  Reduces network load  ISPs are 🙂
  Reduces content download time  Users/customers are 🙂

## Slide 43: Electronic Mail

## Slide 44: Electronic Mail
User Agent
a.k.a. “mail reader”
Composing, editing, reading mail messages
Mail servers:
Mailbox contains incoming messages for user
Message queue of outgoing (to be sent) mail messages
User mailbox
Outgoing
message queue
mail
server
mail
server
mail
server
user
agent
user
agent
user
agent
user
agent
user
agent
user
agent

## Slide 45: Electronic Mail
Mail transfer protocol: Delivery/storage to receiver’s server  Push operation
  SMTP: Simple Mail Transfer Protocol
  User agent to mail server
  In between mail servers
SMTP protocol between mail servers to send email messages
  Client: sending mail server
  “Server”: receiving mail server
Src: https://en.wikipedia.org/wiki/Open_mail_relay#/media/File:Email.svg

## Slide 46
Mail access protocol: retrieval from server  Pull operation
  POP: Post Office Protocol [RFC 1939]: authorization, download
  IMAP: Internet Mail Access Protocol [RFC 1730]: more features, including manipulation of stored messages on server
  HTTP: gmail, Hotmail, Yahoo! Mail, etc.
Src: https://en.wikipedia.org/wiki/Open_mail_relay#/media/File:Email.svg
Electronic Mail

## Slide 47: SMTP
Uses TCP to reliably transfer email message from client (mail server initiating connection) to server, port 25
  Direct transfer: sending server (acting like client) to receiving server
Three phases of transfer
  SMTP handshaking (greeting)
  SMTP transfer of messages
  SMTP closure
Initiate TCP
connection
RTT
220
250 Hello
HELO
SMTP handshaking
“Client”
SMTP server
“Server”
SMTP server
SMTP transfers

## Slide 48: Summary
Web and HTTP:
  Persistent and non-persistent HTTP
  Web cache
Electronic mail:
  SMTP, POP, IMAP